## Slide 1: 9.2 Maneuverability
Important when:
  Station keeping
  UNREP
  Docking
  “Dodging incoming...”
Predicted by:
  Equations of Motion
  Tank Models
Verified by Sea Trials
(Same procedure for aircraft)

## Slide 2
The maneuverability performance of the rudder can be described by three broad categories:
      Directional Stability
      Response
      Slow Speed Maneuverability
Maneuverability

## Slide 3
The ability to continue to travel in a straight line
- With rudder at midships
- With no external pressure acting on the vessel or rudder
Controls Fixed Straight Line Stability
- A condition rarely achieved
Any condition other than heading directly into the seas
will alter the ability to continue straight
Directional Stability

## Slide 4
The ability to continue to travel in a straight line
Longer ships are more likely to possess straight line
stability
Short “beamy” ships, like tugs, small sport craft, have
poor straight line stability
- To improve this, can increase “deadwood” of the ship
- This is the part of the hull that exists in front of
the rudder, an extension of the ship
- Acts like the feathers on an arrow
Directional Stability

## Slide 5
Directional Stability
Straight Line Stability - The ship responds to the disturbance by steadying on some new course.

## Slide 6
The ability to turn the ship when the rudder is applied, and to return the ship to the desired heading with minimal overshoot
When applied, the rudder must be able to change the orientation
of the ship in a minimum set time.
The ship must be able to return on course without going beyond
the desired heading.
Turn Response

## Slide 7
- Responsiveness is determined by the ship’s mission
- A combatant needs high maneuverability
- A merchant ship needs much less than a combatant
- Can quantify responsiveness by the Rudder Area Ratio:
Rudder Area Ratio = Rudder Area
Lpp T
A cargo ship = 0.017,… a destroyer has about 0.025 ratio...
Turn Response

## Slide 8
Turn Response
We want quick response time to helm commands with minimum course overshoot.
Rudder response depends on rudder dimensions, rudder angle, and flow speed.
Directly conflicts with “controls fixed straight line stability”.
Determined during sea trials and tank tests.

## Slide 9
Rudder dimensions limited by space. Larger rudder area means more maneuverability, but more drag.
Rudder angle level of response depends on
standard rudder ordered and available range.
Ship speed determines level of water flow past control surface. Bernoulli’s!
Coxswain Ability
Factors in Turn Response:
Turn Response

## Slide 10
The ability to maneuver at slow speeds < 5 kts
- A ship requires some level of maneuverability at low speeds
- In canals
- Approaching harbor entries
- But as speed drops, so too does rudder control!
Typically requires some additional methods to aid turning and positioning in slow speeds
Slow Speed Maneuverability

## Slide 11
Slow Speed Maneuverability
Must be able to maintain steerageway even at slow speeds.
Directional control systems used at slower speeds.
  Position rudder behind prop (thrust directly on rudder).
    Increases water flow over the rudder
  Twin screws (twist ship).
  Lateral/bow thrusters (research vessels, tugs, merchants and some
  amphibs).
  Rotational thrusters (specialized platforms only).

## Slide 12: Maneuverability Requirements
Maneuverability Trade-Off
  Stability (tendency to stay in a straight line) & maneuverability (ability to easily depart from a straight line) oppose one another
  Large rudders can help both but increase drag
It is not possible to independently optimize each (e.g. good response conflicts with straightline directional stability)!

## Slide 13
9.3 Rudders

## Slide 14
Tip Chord
Root Chord
Hull
Stock
Span
Leading Edge
Trailing Edge
Water Flow
Rudders

## Slide 15
  Chord:
    Horizontal distance from leading to trailing edge
    Limited by propeller and edge of stern
  Span:
    Vertical distance from stock to tip
    Limited by local hull bottom and ship baseline
Chord
Span
Semi-Balanced Spade Rudder
Rudders

## Slide 16: Rudder Balance
Center of Pressure vs. Position of Rudder Stock
  Vertically aligned: “Fully Balanced”
  Rudder Stock at leading edge: “Unbalanced”
  Semi-Balanced
    Less operating torque than unbalanced
    Returns to centerline on failure

## Slide 17
1. Balanced Rudder The rudder stock is positioned toward the center of the rudder, requiring less force to turn the it
Rudder Balance

## Slide 18
2. Unbalanced Rudder The rudder stock is at the leading edge of the rudder
Rudder Balance

## Slide 19
3. Semi Balanced The rudder mounts on a “horn” protruding from the hull
- The top can be considered “unbalanced”
- The bottom can be considered “balanced”
Rudder Balance

## Slide 20
Semi-Balanced Spade Rudder
Rudders

## Slide 21: Rudder Performance
Rudder doesn’t turn ship, hydrodynamics of water flow past ship is
reason for it turning. Rudder flow provides LIFT.
Ship turns by moment produced about the LCP (not LCG)
Center of Pressure

## Slide 22
Stages of a ships turn:
Rudder midships
Rudder is turned
Water Flow
Ship orients itself at the desired angle to oncoming seas
Hull Lift
Rudder Performance

## Slide 23
IT DOES NOT MAKE THE SHIP TURN!
What it DOES do is orient the ship at an angle to the direction of travel…
The pressure on the side of the hull causes the ship to turn (it acts like a flap on an aircraft wing)
Rudder Performance
Rudder Action:
  “Kicks” stern in opposite to desired direction
  Ship’s angle to flow drives ship in desired

## Slide 24: Rudder Performance
Lift produced by force imbalance acts perpendicular to the flow stream.
Lift and drag act at the center of pressure.

## Slide 25
Rudder Performance
Rudder Stall
- Just like an aircraft wing, if the angle of the rudder is too great, the high and lower pressure areas on the rudder will disrupt water flow over the surface
Beyond 45o, the rudder will produce no lift, and so will not effectively orient the ship for turning
Rudder will create turbulence and drag with no effect on ability to turn
- Navy ships typically limit the angle range to about 35o

## Slide 26: Rudder Performance
Keep Rudder angle   35 or STALL likely.
Max Lift Point

## Slide 27: 9.4 Slow Speed Maneuverability
Rudder Pressures or ForcesµV²
Rudder position relative to propeller
Twin propellers
  Stbd: right handed; port: left handed
  Twist ship by operating engines in opposite directions
Lateral/Bow Thrusters
Rotational Thrusters (SPM/Outboard)

## Slide 28: MANEUVERABILITY
The Bottom Line
Good directional stability and minimum ship response conflict, so compromise involved.
Increased rudder area improves response and usually improves directional stability.
Theory and design use many assumptions so empirical testing with models is required.
True test of ship’s maneuverability characteristics is at
Sea Trials.

## Slide 29: Example Problems
Of what is a ship’s directional stability a measure?
Without touching the throttles, the ship slows when we commence a turn; why?
Which of the following helps an operator maneuver the ship at slow speeds (<5kts)?
  Fin stabilizers Deadwood 2 Prop Shafts
  Rotational thrusters Bilge keels Bow thruster
  Small rudder Large rudder

## Slide 30: Example Answers
Of what is a ship’s directional stability a measure?
  Ability to steam in a straight line with the rudder amidships
Without touching the throttles, the ship slows when we commence a turn; why?
  First, when the rudder leaves amidships, it presents a larger cross-section to the flow, increasing drag and resistance, reducing speed for the same EHP.
  Second, when the ship starts to turn, the whole hull now presents a larger cross-section to the flow, amplifying the rudder effect as it “slides” through the turn.
Which of the following helps an operator maneuver the ship at slow speeds (<5kts)?
  Fin stabilizers Deadwood 2 Prop Shafts
  Rotational thrusters Bilge keels Bow thruster
  Small rudder Large rudder